## Slide 1
Predictive Stability Classification
for Smart Electrical Grids
COEN807 Term Project | Supervised Learning | ABU Zaria
Track: Supervised Learning - Binary Classification
Dataset: Electrical Grid Stability Simulated Dataset (Arzamasov et al., 2018)
6 Models Compared | Best: Gradient Boosting Tuned | AUC = 0.9717
Notes: Welcome. This project applies machine learning to classify smart grid stability — stable vs unstable — using 12 electrical parameters. Highly relevant to Nigeria's chronic power infrastructure challenges.

## Slide 2
PROBLEM OVERVIEW
Why Grid Stability Prediction Matters
The Challenge
Nigeria's grid averages only 4,000–5,000 MW actual generation vs 13,000 MW installed capacity, with chronic outages on the 330 kV network (Akorede et al., 2017).
In smart grids, price-responsive consumers create non-linear stability dynamics that conventional eigenvalue analysis cannot assess fast enough for real-time operation.
The Task
Classify each grid configuration from 12 parameters:
UNSTABLE (0)
Eigenvalues with +ve real parts
STABLE (1)
All eigenvalues with −ve real parts
10,000
Instances
6
ML Models
12→18
Features
90%
Best Accuracy
Notes: Emphasise: a missed UNSTABLE prediction = potential cascading blackout. High recall on the Unstable class is the primary operational requirement.

## Slide 3
DATASET
Electrical Grid Stability Simulated Dataset
Source: UCI ML Repository (ID 471) & Kaggle | Ref: Arzamasov et al. (2018) DOI: 10.24432/C5PP49 | 10,000 instances | ZERO missing values
Reaction Times
tau1–tau4
0.5–10.0 s
Time for each node to adjust power in response to a price signal. Shorter = faster response.
Power Values
p1 (gen) p2–p4 (load)
p1: 0.5–2.0 | p2–p4: −2.0– −0.5
Power produced / consumed per node. Negative = drawing from network.
Price Elasticity
g1–g4
0.05–1.00
Demand adjustment per unit price change. Higher g = stronger, faster demand response.
63.0% Unstable (0) - 6,300 instances
37.0% Stable (1) - 3,700 instances
Notes: Star-topology 4-node grid: 1 producer + 3 consumers. The 63/37 class imbalance is moderate — requires weighted metrics, not simple accuracy.

## Slide 4
PREPROCESSING
Data Preprocessing & Feature Engineering
Preprocessing Steps
✓ Data Quality
0 missing values · 0 duplicates · No outliers removed
✓ Stratified Split
80% Train (8,000) · 20% Test (2,000)
Class ratio 63/37 preserved in both sets
✓ StandardScaler
Fit on train only → applied to both
Prevents data leakage
✓ No Encoding
All 12 features already continuous numerical
6 Engineered Features (12 → 18 total)
total_demand
p₂+p₃+p₄
Total consumer load (#1 predictor)
net_power
p₁+total_demand
Generation surplus/deficit
mean_tau
mean(τ₁–τ₄)
Average network response speed
tau_std
std(τ₁–τ₄)
Response time heterogeneity
mean_g
mean(g₁–g₄)
Average price elasticity
response_ratio
mean_g/(mean_τ+ε)
Elasticity÷speed ratio
Notes: Feature engineering was the #1 impact decision — 3 of the top 7 features by RF importance are engineered. total_demand alone = 29% of importance.

## Slide 5
METHODOLOGY
Six Classifiers - Spanning the Bias-Variance Spectrum
LR
Logistic
Regression
Linear baseline · Interpretable
coefficients · C=1.0 L2
DT
Decision
Tree
Rule-based · Non-linear
Human-readable · depth=10
RF
Random
Forest
Bagging ensemble · Feature
importance · n=100 trees
SVM
Support
Vector
Machine
RBF kernel · High-dim
boundary · C=1.0 γ=scale
KNN
K-Nearest
Neighbours
Instance-based · No params
Euclidean · k=5
GB
Gradient
Boosting ★
Boosting ensemble · Best
performance · n=100 lr=0.1
All models: scikit-learn 1.3.0 | random_state=42 | StandardScaler preprocessing
Notes: Deliberately spanning all major algorithm families: linear, tree, bagging, kernel, instance-based, boosting — comprehensive coverage of the bias-variance spectrum.

## Slide 6
EXPERIMENTAL SETUP
Evaluation Protocol & Metrics Justification
Two-Stage Protocol
Stage 1 - Stratified 5-Fold CV (8,000 train instances)
Each fold preserves 63/37 class ratio · Reports mean ± std per model
▼
Stage 2 - Hold-out Test Set (2,000 UNSEEN instances)
Never used in training or tuning · Final unbiased performance
+ GridSearchCV on best model: n_estimators, max_depth, learning_rate (cv=3, F1-weighted, 12 configs)
Why These Metrics?
Accuracy
Baseline only - 63% trivially by always predicting Unstable
Weighted Precision
Quality of positive predictions weighted by class support
Weighted Recall
Coverage of true instances - critical for Unstable class
Weighted F1 ★
PRIMARY metric - balances P & R under class imbalance
ROC-AUC
Threshold-independent discriminative ability
Confusion Matrix
Absolute TP/TN/FP/FN for best model
Notes: WHY these metrics: accuracy would be 63% for a trivial always-predict-Unstable classifier. Weighted F1 is the selector. AUC reveals probability calibration quality. CV std deviation reveals stability.

## Slide 7
RESULTS
Model Performance Comparison - Test Set
Chart: 
| LR | DT | RF | SVM | KNN | GB
CV Accuracy | 0.8731 | 0.8561 | 0.886 | 0.8881 | 0.8489 | 0.9021
Test F1 | 0.8576 | 0.8588 | 0.8863 | 0.8903 | 0.8386 | 0.9028
AUC | 0.9401 | 0.8728 | 0.9599 | 0.9627 | 0.9131 | 0.9704
Summary Table
Model
F1
AUC
LR
0.858
0.940
DT
0.859
0.873
RF
0.886
0.960
SVM
0.890
0.963
KNN
0.839
0.913
GB
0.903
0.970
GB★
0.900
0.972
GB★ = Gradient Boosting after GridSearchCV tuning
Notes: GB wins on CV accuracy (0.9021) and AUC (0.9704). SVM is second. DT's low AUC (0.8728) vs acceptable accuracy shows why AUC matters. KNN suffers from high dimensionality.

## Slide 8
BEST MODEL
GB Tuned ★ - Confusion Matrix & Classification Report
Best Params: n_estimators=200 | max_depth=5 | learning_rate=0.10 | GridSearchCV (3-fold, F1-weighted)
Confusion Matrix
Predicted: Unstable
Predicted: Stable
Actual
Unstable
Actual
Stable
TN = 1,157
FP = 103
FN = 97
TP = 643
N=2,000 | Unstable support=1,260 | Stable support=740
Class-Level Performance
Class
Prec
Rec
F1
Supp
Unstable (0)
0.9226
0.9183
0.9204
1,260
Stable (1)
0.8619
0.8689
0.8654
740
Weighted Avg
0.9002
0.9000
0.9001
2,000
⚠ False Negative Rate = 97/1,260 = 7.70% - requires human verification layer before deployment
Notes: 103 false positives = unnecessary protective actions (safe but annoying). 97 false negatives = missed unstable grids (operational risk). 7.7% FNR is manageable with human-in-the-loop.

## Slide 9
KEY FINDINGS
Feature Importance — What Drives Grid Stability?
Chart: 
| mean_tau (E) | p2 | p3 | p4 | response_ratio (E) | net_power (E) | total_demand (E)
MDI Importance | 0.049 | 0.0529 | 0.0561 | 0.0602 | 0.0847 | 0.1191 | 0.2903
★ Top 3 Are Engineered
total_demand (29.0%) + net_power (11.9%) + response_ratio (8.5%) = 49.4% of RF importance combined.
Power Balance Dominates
total_demand + net_power alone = 40.9%. Generation–demand balance is the primary physical stability driver.
Domain > Tuning
Feature engineering outperformed GridSearchCV as the single highest-impact modelling decision.
(E) = Engineered feature | MDI = Mean Decrease in Impurity (Random Forest)
Notes: This validates the entire feature engineering investment. The engineered features capture physics the raw features don't: total load stress, net power balance, and the elasticity÷speed interaction ratio.

## Slide 10
COMPARATIVE ANALYSIS
Why Gradient Boosting Wins — Cross-Model Insights
GB > RF (AUC 0.970 vs 0.960)
Boosting's sequential residual correction beats bagging when the boundary has moderate non-linearity, each new tree focuses on the hardest-to-classify instances.
SVM > LR (AUC 0.963 vs 0.940)
2.3-pt AUC gap confirms the stability boundary is non-linear. RBF kernel maps features to a separable manifold LR's linear boundary is insufficient.
DT — Lowest AUC (0.873)
Despite 86% accuracy, hard partition boundaries produce poor probability calibration. Proves that AUC and accuracy tell very different stories.
KNN — Dimensionality Penalty
In 18D scaled space, Euclidean distance loses discriminative power. Highest CV variance (σ=0.009) = sensitivity to training fold composition.
Tuning — Marginal Gain (+0.13%)
GB was near-optimal at defaults. GridSearchCV confirmed depth=5 and n=200. Principal benefit: better leaf interaction capture vs. default depth=3.
Practical Implication
90% accuracy + 97.2% AUC is viable for real-time SCADA screening in the Nigerian power grid — with mandatory human verification at the 7.7% FNR threshold.
Notes: Key talking points: (1) Non-linearity confirmed by SVM>LR. (2) Accuracy≠AUC — the DT example. (3) Tuning had marginal effect; feature engineering was the bigger lever. (4) 90% + 97.2% AUC is deployable with human oversight.

## Slide 11
CHALLENGES & LESSONS
Limitations, Ethics & Lessons Learned
Key Limitations
Synthetic data not validated on real TCN SCADA
Static snapshots - no transient/dynamic stability
4-node star ≠ real 330kV mesh network complexity
No uncertainty quantification point predictions only
GB is partially a black box - SHAP needed for deployment
Ethical Considerations
No autonomous actuation mandatory human override required at all times
Load-shedding equity prevent algorithmic bias against rural/low-income communities
Synthetic data bias simulation assumptions become encoded ground truth
Lesson 1: Feature Engineering > Tuning
Engineered features provided larger performance gains than GridSearchCV domain knowledge is irreplaceable
Lesson 2: Metric Choice = Model Ranking
DT competes on accuracy but fails on AUC proves why primary metric must be defined before training
Lesson 3: CV Std Reveals Stability
KNN σ=0.009 vs GB σ=0.005 invisible from a single 80/20 split stratified k-fold is non-negotiable
Notes: Key safety message: the model must SUPPORT human decisions, never replace them. The 7.7% false negative rate is the primary operational risk. Equity in load-shedding is a social justice issue, not just a technical one.

## Slide 12
CONCLUSION & FUTURE WORK
Key Results & Next Steps
90.00%
Best Test Accuracy
(GB Tuned)
0.9717
Best AUC Score
(GB Tuned)
49.4%
Importance from
Engineered Features
7.70%
False Negative Rate
(human check req.)
Conclusion
6 classifiers compared - Gradient Boosting wins on CV accuracy, test F1, and AUC
Feature engineering (12→18) was the single highest-impact decision
ML-based stability screening is viable for Nigerian SCADA with human oversight
Future Research
LSTM / Temporal CNNs for transient stability dynamics
Graph Neural Networks for real mesh grid topologies
SHAP explainability for NERC regulatory compliance
Empirical validation on real TCN PMU SCADA data
Online incremental learning for evolving grid configurations
Dataset: Arzamasov et al. (2018) DOI: 10.24432/C5PP49 | Code: github.com/<Phaena01>/grid-stability-ml | COEN807 · ABU Zaria
Notes: Close with: GB achieves 90% accuracy + 97.17% AUC on 2,000 unseen instances. The next critical step is validation on real PMU data from the Nigerian national grid. All code and results are fully reproducible via GitHub.